## Slide 1: Exercise 4.104
Created by Lauren Taylor (’14)
Edited by Maxine Chan (‘16), Allee Vito (‘17), Doris Chen (‘18), Olivia Young (‘19), Sanna Vedrine (‘23), Austin Kwan (’24), Donovan Cho (‘25)

## Slide 2: Design Goals
Separate E and X
  Both streams may contain up to 10 wt% of the other component
  Neither stream may contain water
Minimize the number of units
Minimize waste

## Slide 3: Design Specifications
Component | Boiling Point (℃))
E | 100
X | 100
Water | 100
Oil | 320
N2 | -196
Assumptions:
Water and oil are immiscible
Oil does not evaporate into N2
Water evaporates into N2 (1.4 wt% H2O vapor in N2 at 20 ℃)
Cannot separate by distillation!
  input stream
  xH20 = 0.95
  xE = 0.03
  xX = 0.02
Notes: Doesn’t look like we are able to separate E and X using distillation

## Slide 4: Which absorber should we use?
1. Oil + N2
Preferentially extract X into N2
Step 2
2. Water + N2
No clear preferential separation
3. Water + Oil
No clear preferential separation
Step 1 (E and X from water to oil)
* Input: Water, E, X
* Target Output: relatively pure E,X
1.
2.
3.
Notes: these graphs show the thermo data for various potential separations depending on what combination of solvents we use between n2, oil, and water
the 2 graphs on the first row describes the separation of e and if we were to use oil and n2. left shows E and right shows X. we see there is a significant difference in the slopes which indicate that there is a potential. we see that relatively no E ends up in N2. therefore there is potential to use n2 and oil to separate e and x from each other.
lowing at middle row – we see the slopes are very similar and there is therefore no clear potential for a meaningful separation
Want to look for graphs where the curves look significantly different. We see this with oil/N2.
Bubble N2 through oil to extract X
Currently have E and X in water…need to get into an oil solution to be able to separate

## Slide 5
Liquid-Liquid
Absorber
Oil 100 wt%
Water 95 wt%
E 3 wt%
X 2 wt%
Water 100 wt%
Oil 95 wt%
E 3 wt%
X 2 wt%
PLAN
E, X from water  oil
X from E and oil  N2
Notes: Assume all E and X get transferred to oil. This isnt a super realistic assumption, but we will make it here

## Slide 6
Liquid-Liquid
Absorber
Water 95 wt%
E 3 wt%
X 2 wt%
Gas-Liquid Stripper
N2 98 wt%
E 0 wt%
X 2 wt%
N2 100 wt%
Oil 97 wt%
E 3 wt%
X 0 wt%
Oil 100 wt%
Water 100 wt%
Oil 95 wt%
E 3 wt%
X 2 wt%
PLAN
E, X from water  oil
X from E and oil  N2

## Slide 7
Liquid-Liquid
Absorber
Water 95 wt%
E 3 wt%
X 2 wt%
Gas-Liquid Stripper
N2 98 wt%
E 0 wt%
X 2 wt%
N2 100 wt%
Oil 97 wt%
E 3 wt%
X 0 wt%
Oil 100 wt%
Water 100 wt%
Oil 95 wt%
E 3 wt%
X 2 wt%
PLAN
E, X from water  oil
X from E and oil  N2

## Slide 8
Liquid-Liquid
Absorber
Oil 95 wt%
E 3 wt%
X 2 wt%
Water 95 wt%
E 3 wt%
X 2 wt%
Gas-Liquid Stripper
N2 98 wt%
E 0 wt%
X 2 wt%
N2 100 wt%
Oil 97 wt%
E 3 wt%
X 0 wt%
Liquid-Gas Separator -50 °C
X 100 wt%
N2 100 wt%
Liquid-Gas Separator 150 °C
E 100 wt%
Oil 100 wt %
Oil 100 wt%
Water 100 wt%
PLAN
E, X from water  oil
X from E and oil  N2

## Slide 9
Liquid-Liquid
Absorber
Oil 95 wt%
E 3 wt%
X 2 wt%
Water 95 wt%
E 3 wt%
X 2 wt%
Gas-Liquid Stripper
N2 98 wt%
E 0 wt%
X 2 wt%
N2 100 wt%
Oil 97 wt%
E 3 wt%
X 0 wt%
Liquid-Gas Separator -50 °C
X 100 wt%
Liquid-Gas Separator 150 °C
E 100 wt%
Oil 100 wt %
Oil 100 wt%
Water 100 wt%
Don’t Be wasteful! 
N2 100 wt%
PLAN
E, X from water  oil
X from E and oil  N2
Notes: So this looks like a good design…but can we improve?

## Slide 10
Liquid-Liquid
Absorber
Oil 95 wt%
E 3 wt%
X 2 wt%
Water 95 wt%
E 3 wt%
X 2 wt%
Gas-Liquid Stripper
N2 98 wt%
E 0 wt%
X 2 wt%
N2 100 wt%
Oil 97 wt%
E 3 wt%
X 0 wt%
Liquid-Gas Separator -50 °C
X 100 wt%
N2 100 wt%
Liquid-Gas Separator 150 °C
E 100 wt%
Oil 100 wt %
Oil 100 wt%
Water 100 wt%
N2 100 wt%
(make up for purge)
Purge
N2 100 wt%

## Slide 11
Liquid-Liquid
Absorber
Oil 95 wt%
E 3 wt%
X 2 wt%
Water 95 wt%
E 3 wt%
X 2 wt%
Chemical Process
N2 98 wt%
E 0 wt%
X 2 wt%
N2 100 wt%
Oil 97 wt%
E 3 wt%
X 0 wt%
Liquid-Gas Separator -50 °C
X 100 wt%
N2 100 wt%
Liquid-Gas Separator 150 °C
E 100 wt%
Oil 100 wt %
Oil 100 wt%
Water 100 wt%
N2 100 wt%
(make up for purge)
Purge
Oil 100 wt %
Oil 100 wt%
(make up stream)
Gas-Liquid Stripper
Purge
N2 100 wt%

## Slide 12: Key Takeaways
The oil/water and oil/N2 extractions are not perfect
Minimize flow rates by recycling solvents when possible!