## Slide 1: Exercise 5.22
Created by: McKenzie Huston (‘14)
Edited by: Bari Grossman (‘15), Maxine Chan (‘16),Robert Lee (‘17), Ameer Basrai (’18),Sydney Brannan (‘19),Sabrina Chen (‘20),Apoorva Agarwal (‘21),Sarah Huang (‘22),Ariel Struzyk (‘23), Burke Combs (‘24),Lauren de Silva (‘25)

## Slide 2
This is your first real introduction to dimensionless numbers….
Don’t worry…you’ll apply them more next semester!

## Slide 4
Lauren- Lewis number
Le =
“same name as my dad”
Your TA’s Favorite Dimensionless Groups
Dennis- Damkhӧler number
“ idk it has a fun ӧ ”
Ashlyn- Reynolds number
“cause it’s the only one I remember ”
Donny- Mach number
“because its easy”

## Slide 5
Parameter | Symbol
Density difference | Δρ
Surface tension | γ
Characteristic size | d
Gravitational acceleration | g
Base Dimension | Abbreviation
Length | L
Mass | M
Time | T
Temperature | Θ
Amount | N
Dimensions
M/L3
L
L/T2
Unit
= kg/L
= N/m
distance = m
= m/s2
Unit
distance = m
We need these dimensions!
(A): Derive the Bond Number, Bo

## Slide 6
When writing out the dimensions of some variable of interest or group of variables, we use the following notation:
Using the gravitational constant as an example, we have . For any dimensionless group, we can write
Aside: Important Notations

## Slide 7
Base Dimension | Abbreviation
Length | L
Mass | M
Time | T
Temperature | Θ
Amount | N
Deriving dimensions of surface tension

## Slide 8
Parameter | Symbol
Density difference | Δρ
Surface tension | γ
Characteristic size | d
Gravitational acceleration | g
Base Dimension | Abbreviation
Length | L
Mass | M
Time | T
Temperature | Θ
Amount | N
Dimensions
M/L3
M/T2
L
L/T2
Unit
= kg/L
= N/m
distance = m
= m/s2
Unit
distance = m
Let’s solve using the formal method!

## Slide 9: Formal Method
Mass: a + b = 0
Length: –3a + c + d = 0
Time: –2b – 2d = 0
We know:
4 parameters – 3 equations = 1 Π group
Exponent of g is 1, so d = 1

## Slide 10
Solve equations:
a = 1
b = –1
c = 2
d = 1
Check the dimensions of Bo:

## Slide 11: (B): Derive the Capillary Number, Ca
Parameter | Symbol
Fluid velocity | ν
Fluid viscosity | μ
Surface tension | γ
Base Dimension | Abbreviation
Length | L
Mass | M
Time | T
Temperature | Θ
Amount | N
Dimensions
L/T
M/LT
M/T2
Unit
Unit

## Slide 12: Informal Method
We know that the exponent of ν is 1.
The only other term with L is μ term. For L to cancel, b must equal 1, so
Combining the two known terms, we have
Therefore, c = -1

## Slide 13: Formal and informal methods give the same answer!
Mass: b + c = 0
Length: a – b = 0
Time: –a – b – 2c = 0
3 parameters – 3 equations = 0 Π groups
But wait, these equations are not independent!
–(a – b) – 2(b + c) = –a – b – 2c
Solve:
a = 1
b = 1
c = –1
3 parameters – 2 equations = 1 Π group
Formal Method

## Slide 14
Let’s check our answer…

## Slide 15
There are two valid methods to solve for dimensionless groups:
Formal method: write out expressions for dimensions, then solve algebraically
Informal method: use what you know and relationships between variables to deduce exponents
Solution Method Summary

## Slide 16
Units and dimensions are the same thing!
Don’t confuse units and dimensions!
Verify you use the correct dimensions!
Carefully work the algebra!
Check your final answer to ensure it is dimensionless.
5.22: Key Takeaways