## Slide 1: Calculation Session 1 Exercise 2.22
Created by Yuan Li (‘12)
Revised by Katie Reilly (’12), Andrew Broenen (‘13), Lauren Taylor (‘14), Carl Schultz (‘15), Maxine Chan (‘16)/Jesse Garcia (’16), Robert Lee (‘17), Ameer Basrai (‘18), Francis Ledesma (‘19), Michelle Quien (‘20)/Ian Morrison (‘20), Ann Metzloff (‘21), Sarah Huang (’22), Sanna Vedrine (‘23), Austin Kwan (‘24), Dennis Wu (‘25), Amy Wu (‘26)
Notes: hope you have had enough time work on this exercise – I will now start going over part a.

## Slide 2: Exercise Overview
Design a process to efficiently transport natural gas
  Produce methanol from methane and water
Fracking
Utility Company
Notes: methanol is an easily transportable liquid
methanol  energy form is easier to transport and a better fuel source than methane (more attractive and valuable

## Slide 3: What are we given?
Design Goals
Produce methanol from methane and water
Minimize number of units at 300 atm
Design Rules
Only use given chemistry!
Assume no reactions go to completion (80-90%)
Assume ideal separations:
  Solid-liquid
  Solid-gas
Show compressors/expanders

## Slide 4: Our Reactions
(A)
900 ᵒC
300 ᵒC
300 atm
Notes: You can use colors to track where each compound goes.

## Slide 5
H2O
CH4
Steam-Methane Reformer
900 ᵒC
H2O
CH4
CO
H2
Methanol Synthesis Reactor
300 ᵒC, 300 atm
CH3OH
Does this satisfy the
design goals and rules?
Design Goal
Produce methanol from methane and water
Minimize number of units at 300 atm
Design Rules
Only use given chemistry!
Assume no reactions go to completion (80-90%)
Assume ideal separations:
  Solid-liquid
  Solid-gas
Show compressors/expanders
(A)
Notes: What can be done? Add unreacted reagents

## Slide 6
H2O
CH4
Steam-Methane Reformer
900 ᵒC
H2O
CH4
H2O
CH4
CO
H2
Methanol Synthesis Reactor
300 ᵒC, 300 atm
H2O
CH4
CO
H2 CH3OH
For example, we waste valuable
reactor space on unused reagents
(H2O, CH4) the 2nd reactor.
What should we do to fix this?
Add a separator!
Does this satisfy the
design goals and rules now?
Almost… we can still improve the process.
(A)
300 atm
1 atm
H2O
CH4
CO
H2
Notes: considering that none of the reactions go to completion, how many components will be in the exit stream – hold
What can be done? Add a separator. The compressor and reactor become smaller, which is much cheaper.

## Slide 7
H2O
CH4
Steam-Methane Reformer
900 ᵒC
H2O
CH4
CO
H2
CH4
H2O
CH4
H2O
CO
H2
Methanol Synthesis Reactor
300 ᵒC, 300 atm
Separator
CH3OH
CO
H2
Can have a smaller reactor now!
Is this separation possible? If so, what temperature?
(A)
300 atm
1 atm
CO
H2
Notes: Don’t need unreacted reagents, separate them!
Can this separation be achieved? Let’s look at the boiling points of these compounds.

## Slide 8: Physical Properties
Compound | Melting Point (oC) | Boiling Point (oC)
CH4 | -182 | -164
H2O | 0 | 100
CO | -205 | -191
H2 | -259 | -253
CH3OH | -94 | 65
Is there another way to visualize this information?
(A)

## Slide 9: Physical Properties
0oC
100oC
-300oC
-100oC
-200oC
0oC
100oC
-300oC
-100oC
-200oC
0oC
100oC
-300oC
-100oC
-200oC
0oC
100oC
-300oC
-100oC
-200oC
H2
CO
CH4
H2O
-170 ᵒC
Separator
CH4
H2O
CO
H2
CO
H2 CH4
H2O
SOLID
LIQUID
VAPOR
(A)
Notes: I think that a color-coded chart like this is useful to visualize the physical properties. Here. green = solid, blue = liquid, red = gas. It’s now easy to see that at ~ -170 oC, the CO and H2 will be gases, and can be separated from the liquid CH4 and solid H2O.

## Slide 10
H2O
CH4
Steam-Methane Reformer
900 ᵒC
H2O
CH4
CO
H2
CH4
H2O
CH4
H2O
CO
H2
Methanol Synthesis Reactor
300 ᵒC, 300 atm
CH3OH
CO
H2
(S & L)-G Separator
-170 ᵒC
CH3OH
CO
H2
Have we reached our design goal?
Not quite…Pure methanol is our desired product! We need a separator!
(A)
CO
H2
Notes: CH4 is liquid, H2O is solid. CO and H2 are gases. Also don’t need these unreacted reagents!

## Slide 11
H2O
CH4
Steam-Methane Reformer
900 ᵒC
H2O
CH4
CO
H2
CH4
H2O
CH4
H2O
CO
H2
Methanol Synthesis Reactor
300 ᵒC, 300 atm
CH3OH
CO
H2
CO
H2
(S & L)-G Separator
-170 ᵒC
Separator
CH3OH
(A)
CO
H2
Notes: Don’t forget about compressors and expanders! We want to minimize the number of units at high pressure. Let’s prevent the separator from operating at 300 atm.

## Slide 12: Physical Properties
0oC
100oC
-300oC
-100oC
-200oC
0oC
100oC
-300oC
-100oC
-200oC
0oC
100oC
-300oC
-100oC
-200oC
H2
CO
CH3OH
Question: Should we separate at -150 oC or 20 oC?
20 oC (room temperature)
Cooling to -150 oC requires unnecessary energy to achieve the same separation
20 ᵒC
-150 ᵒC
Separator
CH3OH
CO
H2
CO
H2 CH3OH
SOLID
LIQUID
VAPOR
(A)
Notes: The separation can be easily achieved because the boiling points are vastly different.
Should we put it at -150 degrees? NO! Takes too much energy and thus cost, put it at room temperature (in the problem statement).

## Slide 13
H2O
CH4
Steam-Methane Reformer
900 ᵒC
H2O
CH4
CO
H2
CH4
H2O
CH4
H2O
CO
H2
Methanol Synthesis Reactor
300 ᵒC, 300 atm
CH3OH
CO
H2
CO
H2
(S & L)-G Separator
-170 ᵒC
L-G Separator
20 ᵒC, 300 atm
CH3OH
Does this process satisfy the design goal?
No, need to minimize units at 300atm
Does this process satisfy the design rules?
No, need compressor & expander
(A)
CO
H2
Notes: Don’t forget about compressors and expanders! We want to minimize the number of units at high pressure. Let’s prevent the separator from operating at 300 atm.

## Slide 14
H2O
CH4
Steam-Methane Reformer
900 ᵒC
H2O
CH4
CO
H2
CH4
H2O
CH4
H2O
CO
H2
1 atm
Methanol Synthesis Reactor
300 ᵒC, 300 atm
CH3OH
CO
H2
(S & L)-G Separator
-170 ᵒC
L-G Separator
20 ᵒC
300 atm
CO
H2
300 atm
CH3OH
CO
H2
1 atm
CO
H2
CH3OH
Does this process satisfy the design goals and rules?
Yes, but we can still improve the process!
(A)
Recycle
starting material and intermediates
Notes: Not a bad setup. Can this be improved?
Recycle the CO and H2.

## Slide 15
H2O
CH4
Steam-Methane Reformer
900 ᵒC
H2O
CH4
CO
H2
CH4
H2O
CH4
H2O
CO
H2
1 atm
Methanol Synthesis Reactor
300 ᵒC, 300 atm
CH3OH
CO
H2
(S & L)-G Separator
-170 ᵒC
L-G Separator
20 ᵒC
300 atm
CO
H2
300 atm
CH3OH
CO
H2
1 atm
CO
H2
CH3OH
CO
H2
What do all recycles need?
All recycles need purges!
(A)
Notes: What do all recycles need? Purges.

## Slide 16
H2O
CH4
Steam-Methane Reformer
900 ᵒC
H2O
CH4
CO
H2
CH4
H2O
CH4
H2O
CO
H2
1 atm
Methanol Synthesis Reactor
300 ᵒC, 300 atm
CH3OH
CO
H2
(S & L)-G Separator
-170 ᵒC
L-G Separator
20 ᵒC
300 atm
CO
H2
300 atm
CH3OH
CO
H2
1 atm
CO
H2
CH3OH
CO
H2
Purge
Purge
Let’s check the overall reaction!
(A)
CH4
H2O
CO
H2
Notes: Always check the mass balance!

## Slide 17: Overall Reaction
What we want!
Extra
MUST Agree with Overall Process...
(A)
Notes: To see the overall reaction we add the two reactions and cancel substances that appear on both the left and right sides
The overall reaction MUST agree with the overall process! And from that we see that CH4 and H2O must enter our process, and CH3OH and H2 must leave the process. Is that what we have?

## Slide 18
H2O
CH4
Steam-Methane Reformer
900 ᵒC
H2O
CH4
CO
H2
CH4
H2O
CH4
H2O
CO
H2
1 atm
Methanol Synthesis Reactor
300 ᵒC, 300 atm
CH3OH
CO
H2
(S & L)-G Separator
-170 ᵒC
L-G Separator
20 ᵒC
300 atm
CO
H2
300 atm
CH3OH
CO
H2
1 atm
CO
H2
CH3OH
CO
H2
Purge
Purge
No H2 stream leaves the process!
(A)
CH4
H2O
CO
H2
Notes: No!
This design has an error: the overall process does not agree with the overall reaction.

## Slide 19: Problem: H2 will accumulate in the process  need an outlet
Does the purge after the CH3OH separator solve the problem?
No! Because the purge also removes CO, it does not solve the problem of excess H2.
What could we do?
Add a separator to remove pure H2, which we can sell!
(A)
Notes: For the purge to solve the problem, the H2/CO ratio in the recycle (and in the CH3OH synthesis reactor) would need to be large. This would increase the volume of the high-pressure reactor, which would be expensive.

## Slide 20
H2O
CH4
Steam-Methane Reformer
900 ᵒC
H2O
CH4
CO
H2
CH4
H2O
CH4
H2O
CO
H2
1 atm
Methanol Synthesis Reactor
300 ᵒC, 300 atm
CH3OH
CO
H2
(S & L)-G Separator
-170 ᵒC
L-G Separator
20 ᵒC
300 atm
CO
H2
300 atm
CH3OH
CO
H2
1 atm
CO
H2
CH3OH
CO
H2
Purge
Purge
What temperature and location for the separator?
(A)
CH4
H2O
CO
H2
Notes: Always check the mass balance!

## Slide 21: Physical Properties
0oC
100oC
-300oC
-100oC
-200oC
0oC
100oC
-300oC
-100oC
-200oC
H2
CO
-195 oC
SOLID
LIQUID
VAPOR
Separator
CO
H2
CO
H2
(A)
Notes: Condensing CO requires a temperature below -191 oC. Let’s choose -195 oC. This is best done immediately after the first separator, which operates at -170 oC.

## Slide 22
H2O
CH4
Steam-Methane Reformer
900 ᵒC
H2O
CH4
CO
H2
CH4
H2O
CH4
H2O
CO
H2
1 atm
Methanol Synthesis Reactor
300 ᵒC, 300 atm
CH3OH
CO
H2
(S & L)-G Separator
-170 ᵒC
L-G Separator
20 ᵒC
300 atm
CO
H2
300 atm
CH3OH
CO
H2
1 atm
CO
H2
CH3OH
CO
H2
Purge
Purge
What temperature and location for the separator?
- 195 ºC
After 1st separator
(A)
CH4
H2O
CO
H2
Notes: Always check the mass balance!

## Slide 23
H2O
CH4
Steam-Methane Reformer
900 ᵒC
H2O
CH4
CO
H2
CH4
H2O
CH4
H2O
CO
H2
1 atm
Methanol Synthesis Reactor
300 ᵒC, 300 atm
CH3OH
CO
H2
(S & L)-G Separator
-170 ᵒC
L-G Separator
20 ᵒC
300 atm
CO
H2
300 atm
CH3OH
CO
H2
1 atm
CO
H2
CH3OH
CO
Purge
Purge
H2
H2
H2
CO
H2
L-G Separator
-195 ᵒC
What ratio for splitter?
(A)
CH4
H2O
CO
H2
Notes: This setup accounts for the extra H2 produced.
Last thing to consider: what ratio should we split it at?

## Slide 24: Overall Reaction
For every 1 mol of reactants of the first reaction, 3 mols of hydrogen are produced
For every 1 mol of product produced by the second reaction, 2 mols of hydrogen are consumed
Therefore, 1 mol of hydrogen goes unused, while 2 mols are needed for reaction
(A)
Notes: Read the text^

## Slide 25
H2O
CH4
Steam-Methane Reformer
900 ᵒC
H2O
CH4
CO
H2
CH4
H2O
CH4
H2O
CO
H2
1 atm
Methanol Synthesis Reactor
300 ᵒC, 300 atm
CH3OH
CO
H2
(S & L)-G Separator
-170 ᵒC
L-G Separator
20 ᵒC
300 atm
CO
H2
300 atm
CH3OH
CO
H2
1 atm
CO
H2
CH3OH
CO
Purge
Purge
H2
H2
H2
CO
H2
L-G Separator
-195 ᵒC
Splitter 1:2
(A)
CH4
H2O
CO
H2
Notes: And so we should split it 1:2 – removing one third of the stream and directing two thirds back into the process!

## Slide 26: Process Overview
Goal: synthesize (and isolate) pure methanol
Since reactions don’t go to completion we used separators, recycles (and purges) to improve process
Make incremental modifications
  Have you satisfied the design goals and rules?
    Minimizing # of units at 300 atm
  Checking overall reactions
  Recycle with purges!
(A)

## Slide 27: Oh no!... Side Reactions
Steam-Methane Reformer
900 C
H2O (excess)
CH4
CO
H2
H2O
CH4
(B)
CO2
Notes: In part B we take side reactions into account. We try to avoid the disproportionation CO+CO reaction, so instead we use the water gas shift.
This reaction introduces CO2 as a product in the first reactor.

## Slide 28: What else do we know?
Water gas shift creates CO2 side product
  CO2 can be converted to CO in the methanol synthesis reactor if H2O is not present
  Reconversion is not complete
(B)

## Slide 29
H2O
CH4
Steam-Methane Reformer
900 ᵒC
H2O (excess)
CO
H2
CH4
H2O
CO
H2
1 atm
Methanol Synthesis Reactor
300 ᵒC, 300 atm
CH3OH
CO
H2
(S & L)-G Separator
-170 ᵒC
L-G Separator
20 ᵒC
300 atm
CO
H2
300 atm
CH3OH
CO
H2
1 atm
CO
H2
CH3OH
CO
Purge
H2
H2
H2
CO
H2
L-G Separator
-195 ᵒC
Splitter 1:2
CO2
S-G Separator
CH4
H2O
CO2
CH4
What temperature?
(B)
CO
H2
Notes: To avoid disproportionation, put the water in excess, and add co2 as a product.
Looking at boiling points, we know CO2 will come out the bottom with methane and water because co2 has a higher boiling point than methane.
Thinking about our principle of recycling unused reactant, should we separate the methane or the water out with the co2? (water)

## Slide 30: Physical Properties
0oC
100oC
-300oC
-100oC
-200oC
CO2
0oC
100oC
-300oC
-100oC
-200oC
0oC
100oC
-300oC
-100oC
-200oC
CH4
H2O
-85 ᵒC
SOLID
LIQUID
VAPOR
(B)
Notes: CO2 is between methane and water, but we don’t need methane at all for the second reactor, while we do need water for the second reactor.
Pick a temperature between methane and co2

## Slide 31
H2O
CH4
Steam-Methane Reformer
900 ᵒC
H2O (excess)
CO
H2
CH4
H2O
CO
H2
1 atm
Methanol Synthesis Reactor
300 ᵒC, 300 atm
CH3OH
CO
H2
(S & L)-G Separator
-170 ᵒC
L-G Separator
20 ᵒC
300 atm
CO
H2
300 atm
CH3OH
CO
H2
1 atm
CO
H2
CH3OH
CO
Purge
Purge
H2
H2
H2
CO
H2
L-G Separator
-195 ᵒC
Splitter 1:2
CO2
CH4
S-G Separator
CO2
H2O
CH4
H2O
CO2
CH4
-85 ᵒC
Where should CO2 and H2O go?
(B)
CH4
CO
H2
Notes: So now we’re sending the co2 and water to the L-G separator, since sending it anywhere else would be efficient and take up space at such high pressures
Where does CO2 and water go at this temperature?

## Slide 32: Side Reactions
Methanol Synthesis Reactor 300 C
300 atm
CO2
CO
H2
CO2
CO
H2
H2O
CH3OH
(B)
Notes: To get CO back from CO2, we use the reverse shift reaction. This requires no water in the reactor at the beginning.
Write the new products into the outlets of the reactors and trace them through the process (e.g. separators). What needs to be fixed?

## Slide 33
H2O
CH4
Steam-Methane Reformer
900 ᵒC
H2O (excess)
CO
H2
CH4
H2O
CO
H2
1 atm
Methanol Synthesis Reactor
300 ᵒC, 300 atm
CH3OH
CO
H2
(S & L)-G Separator
-170 ᵒC
L-G Separator
20 ᵒC
300 atm
CO
H2
300 atm
CH3OH
CO
H2
1 atm
CO
H2
CH3OH
CO
Purge
Purge
H2
H2
H2
CO
H2
L-G Separator
-195 ᵒC
Splitter 1:2
CO2
CH4
S-G Separator
CO2
H2O
CH4
H2O
CO2
CH4
-85 ᵒC
Where do the CO2 and H2O go?
(B)
CO
H2
CH4
Notes: So now we’re sending the co2 and water to the L-G separator, since sending it anywhere else would be inefficient and take up space at such high pressures
Where does CO2 and water go at this temperature?

## Slide 34: Physical Properties
0oC
100oC
-300oC
-100oC
-200oC
0oC
100oC
-300oC
-100oC
-200oC
0oC
100oC
-300oC
-100oC
-200oC
H2
CO
CH3OH
0oC
100oC
-300oC
-100oC
-200oC
CO2
0oC
100oC
-300oC
-100oC
-200oC
H2O
20 ᵒC
SOLID
LIQUID
VAPOR
(B)
Notes: The separation can be easily achieved because the boiling points are vastly different.
Should we put it at -150 degrees? NO! Takes too much energy and thus cost, put it at room temperature (in the problem statement).

## Slide 35
H2O
CH4
Steam-Methane Reformer
900 ᵒC
H2O (excess)
CO
H2
CH4
H2O
CO
H2
1 atm
Methanol Synthesis Reactor
300 ᵒC, 300 atm
CH3OH
CO
H2
(S & L)-G Separator
-170 ᵒC
L-G Separator
20 ᵒC
300 atm
CO
H2
300 atm
CH3OH
CO
H2
1 atm
CO
H2
CH3OH
CO
Purge
Purge
H2
H2
H2
CO
H2
L-G Separator
-195 ᵒC
Splitter 1:2
CO2
CO2
CH4
S-G Separator
-85 ᵒC
CO2
H2O
CO2
CO2
H2O
CH4
H2O
CO2
CH4
Need to isolate methanol!
(B)
CO2
CO
H2
CH4
CO2
H2O
CO2
H2O
Notes: Add your new components to the reaction streams, and now we can pay attention to the next side reaction

## Slide 36
H2O
CH4
Steam-Methane Reformer
900 ᵒC
H2O (excess)
CO
H2
CH4
H2O
CO
H2
1 atm
Methanol Synthesis Reactor
300 ᵒC, 300 atm
CH3OH
CO
H2
(S & L)-G Separator
-170 ᵒC
L-G Separator
20 ᵒC
300 atm
CO
H2
300 atm
CH3OH
CO
H2
1 atm
CO
H2
CH3OH
CO
Purge
Purge
H2
H2
H2
CO
H2
L-G Separator
-195 ᵒC
Splitter 1:2
CO2
CO2
CH4
S-G Separator
-85 ᵒC
CO2
H2O
CO2
CO2
CO2
H2O
CO2
H2O
H2O
CH4
H2O
CO2
L-G Separator
CH4
(B)
CH4
CO
H2
CO2
Notes: Now we have our new products, with carbon dioxide and water, which we trace through the streams
We know that water comes out with methanol, so all the water from this reactor will come out the separator
Finally, we should separate the water from the methanol to get our pure desired product: what temperature?

## Slide 37: Physical Properties
0oC
100oC
-300oC
-100oC
-200oC
CH3OH
0oC
100oC
-300oC
-100oC
-200oC
H2O
80 ᵒC
SOLID
LIQUID
VAPOR
(B)
Notes: The separation can be easily achieved because the boiling points are vastly different.
Should we put it at -150 degrees? NO! Takes too much energy and thus cost, put it at room temperature (in the problem statement).

## Slide 38
H2O
CH4
Steam-Methane Reformer
900 ᵒC
H2O (excess)
CO
H2
CH4
H2O
CO
H2
1 atm
Methanol Synthesis Reactor
300 ᵒC, 300 atm
CH3OH
CO
H2
(S & L)-G Separator
-170 ᵒC
L-G Separator
20 ᵒC
300 atm
CO
H2
300 atm
CH3OH
CO
H2
1 atm
CO
H2
CH3OH
CO
Purge
Purge
H2
H2
H2
CO
H2
L-G Separator
-195 ᵒC
Splitter 1:2
CO2
CO2
CH4
S-G Separator
-85 ᵒC
CO2
H2O
CO2
CO2
CO2
H2O
CO2
H2O
H2O
CH4
H2O
CO2
L-G Separator
80 ᵒC
CH3OH
H2O
H2O
CH4
Purge
(B)
H2O
CH4
CO
H2
CO2
H2O
CH4
Notes: Should we just throw away this water? NO
Recycle!

## Slide 39: Process Overview
Utilize new reactions to prevent unfavorable side reaction
Isolate pure methanol
Recycle unused reactants
Check overall reaction
(B)

## Slide 40: Summary
Key Takeaways
  Overall reaction needs to be represented in overall process
  Minimize size of costly units via separations
  Place separators strategically for optimal energy efficiency
  Minimize inlet flow and waste by using recycles
  Every recycle needs a purge!
Problem Solving Strategies
  Start with overall reaction, think about how overall process should go
  Underline/color code important information
  Check overall reaction at the end