## Slide 1: Calculation Session 2 Exercise 2.34
Created By:
Alana Szkodny (‘14)
Tim Abbott (‘15)
Alex Settle (‘16)
Jenny Bushnell (‘17)
Akash Vaidya (‘18)
Joe Hassler (‘18)
Sydney Brannan (‘19)
Gavin Batsimm (‘21) + Apoorva Agarwal (‘21)
Kelsey Levine (‘22)
Leon Lee (‘23)
Burke Combs (‘24)
Lauren de Silva + Dennis Wu (‘25)
Lara Capellino (‘26)
Notes: 1

## Slide 2
Reactions
Desired, 90% conversion
Undesired, 100% conversion
F and G in the product stream!
Only B in the product stream!
We are given:
Feed Stream
1000 mol/min H20
  1 mol/min F
  2 mol/min I
(2) Pure G (unlimited flow rate)
Physical Parameter Data
“What happens along the way”
“Where I start”
“How I reach my targets”
Notes: We’re also given a bunch of other information in the problem statement.
[click] First, we’re given the all-important chemical reactions and [click]their % conversions. What do these % conversions mean? It tells us what percentage of the compounds are converted to products.
In the scope of this problem, the 90% conversion implies that [click] F and G will be in the product stream from the reactor, but I won’t! This means that we’re going to have leftover reactant that needs to be purified.
We’re also given [click] flow rates for the two input streams (pay close attention to the unlimited flow rate for G), and [click] the physical parameter data.
Note the fact that B, our only by-product, is worth 40x less than P,
need 3 mols of G to consume all reactant

## Slide 3: Goals for Our Design
Produce product
Minimize the number (and size) of units
Maximize and other valuable by-products
Employ easy separations
Decreasing Importance
Decreasing Importance

## Slide 4
F 1 mol/min
I 2 mol/min
H2O
Let’s start at the beginning
Initial strategy…
Remove I and H2O from the feed stream. This way we can easily make P from F+G and reduce the size of our units!
Problem: Purify by separating it from
Notes: Speaker 1 Proposes that the problem statement is to purify F by separating it from I

## Slide 5
Solution Methods: Separation tools we’ve seen
1. Phase: Gas- Liquid Separation
2. Phase: Solid- Liquid Separation
3. Chemistry: Exploit Different Reactivities
Notes: Pause and ask students which tools they can recall.
See Lecture 3!

## Slide 6
To separate I from F, could we use:
    1. Liquid/gas separation?
Nope.
-40 -20 0 20 40 60 80 100 120 140
F
°C
-40 -20 0 20 40 60 80 100 120 140
I
°C
Solution Methods: Purifying F
Notes: 6

## Slide 7
To separate I from F, could we use:
    1. Liquid/gas separation?
    2. Solid/liquid separation?
Maybe!
-40 -20 0 20 40 60 80 100 120 140
F
°C
-40 -20 0 20 40 60 80 100 120 140
I
°C
Solution Methods: Separations
Notes: 7

## Slide 8
To separate I from F, could we use:
    1. Liquid/gas separation?
    2. Solid/liquid separation?
Solution Methods: Separations
solid/liquid separator
50˚C
F
I
H2O
F (aq)
H2O
I (s)
Could we remove the water beforehand?
Notes: 8

## Slide 9
To separate I from F, could we use:
    1. Liquid/gas separation?
    2. Solid/liquid separation?
-40 -20 0 20 40 60 80 100 120 140
F
°C
-40 -20 0 20 40 60 80 100 120 140
I
°C
Solution Methods: Separations
Let’s separate water using a L/G separator!
Notes: 9

## Slide 10
To separate I from F, could we use:
    1. Liquid/gas separation?
    2. Solid/liquid separation?
Solution Methods: Separations
F 1 mol/min
I 2 mol/min
H2O
liquid/gas separator
110˚C
solid/liquid separator
50˚C
Steam
F (liq) 1 mol/min
I (liq) 2 mol/min
F (liq)
I (s)
F (liq)
Would this work?
Notes: 10

## Slide 11
Demonstration Time!
Can you think of an example from daily life? Anything similar to what you might encounter in industry?
TAs Amy and Kong do…

## Slide 13
To separate I from F, could we use:
    1. Liquid/gas separation?
    2. Solid/liquid separation?
Solution Methods: Separations
F 1 mol/min
I 2 mol/min
H2O
liquid/gas separator
110˚C
solid/liquid separator
50˚C
Steam
F (liq) 1 mol/min
I (liq) 2 mol/min
F (liq)
I (s)
F (liq)
<< 1 mol/min
~ 2 mol/min
~ 1 mol/min
This won’t work either! With a high solid-to-liquid ratio, most of F (liq) will be absorbed in I (s) 
Notes: 13

## Slide 14
pause
maybe there’s another way to think about this
Notes: Since the easy phase separations lead us to a dead end, maybe lets try thinking about this exercise differently.

## Slide 15
Let’s go back to the beginning
Main goal: Produce product
Do we need to remove?
No!
Redefined Problem: Produce product
Problem: Purify by separating it from

## Slide 16
reactor
20°C
G (excess)
F (aq)
I (aq)
H2O
F (aq)
I (aq)
G (aq)
H2O
F (aq)
G (aq)
P (aq)
B (aq)
H2O
Option #1
Trying again, just trying to produce P
100% conversion
90% conversion

## Slide 17
Trying again, just trying to produce P
Option #2
F (aq)
I (aq)
H2O
steam
F
I
G (excess)
FG
I
F
G
B
P
liquid/gas separator
110˚C
reactor
20°C
Even though Option 2 has 1 extra unit, all subsequent units will be smaller in 2 than 1 and therefore cheaper!
Notes: But dennis, doesn’t your option has 2 units but mine only has 1

## Slide 18
G (excess)
F
G
I
purge
F
G
B
F
G
B
P
P (g)
P (liq)
to market
F
G
B
B
reactor
20°C
liquid/gas separator
65˚C
Option 2A
F (aq)
I (aq)
H2O
steam
F
I
liquid/gas separator
110˚C
Add a liquid-gas separator to produce pure P
Produce P
Can we make it better?
Option #2

## Slide 19
G (excess)
F
G
I
purge
F
G
B
F
G
B
P
P (g)
P (liq)
to market
F
G
B
B
reactor
20°C
liquid/gas separator
65˚C
Option 2A
F (aq)
I (aq)
H2O
steam
F
I
liquid/gas separator
110˚C
Add a heat exchanger to recycle heat and save energy
H2O
H2O
F (aq)
I (aq)
Produce P
Can we make it better?
Option #2a

## Slide 20
L/G Sep. 110˚C
Reactor
F + G → P
I + G → B
20˚C
H2O
F (aq)
I (aq)
H2O
F (aq)
I (aq)
L/G Sep.
65˚C
steam
H2O
F
I
G (excess)
F
G
I
purge
F
G
F
G
B
P
P (g)
P (liq)
to market
F
G
B
L/G Sep. ??˚C
B (g)
F (liq)
G (liq)
B (g)
B
-40 -20 0 20 40 60 80 100 120 140
F, ˚C
-40 -20 0 20 40 60 80 100 120 140
G, ˚C
-40 -20 0 20 40 60 80 100 120 140
B, ˚C
L/G Sep. 85˚C
Produce P
Can we make it better?
Add an additional separator to get product B!
Option #2b
Notes: 2B

## Slide 21
P (liq) to market
Reactor
F + G → P
20 °C
H2O
F (aq)
I (aq)
H2O
F (aq)
I (aq)
L/G Sep.
110 °C
Reactor
F + G → P
I + G → B
20 °C
L/G Sep.
65 °C
steam
H2O
F (liq)
I (liq)
G (excess)
F
G
I
F (liq)
G (liq)
B (liq)
F
G
B
P
P (g)
P (liq) to market
L/G Sep.
85 °C
F
G
B
B (g)
F
G
P (g)
F
G
B
P
B
purge
F
G
F
G
P
F (l)
G (l)
F
G
F
G
P
L/G Sep.
65 °C
Produce P
Can we make it better?
??
Option #2c
Add an additional reactor to produce more P?
Notes: Right off the bat, we have two ways to move forward. We can either just mix excess G with the input stream and react away, or we can remove the water and then react the compounds.
[click] Which option is better? Well, let’s take a look at both of them to find out!
[click] keeping our design principles in mind, let’s go with option 1 and reduce the number of units we have.
21

## Slide 22
Design | 2A | 2B | 2C
# reactors | 1 | 1 | 2
# heat exchangers | 2 | 3 | 4
# separators | 2 | 3 | 4
Total # process units | 5 | 7 | 10
Comparing Our Three Designs

## Slide 23
Option 2C has extra units and is not economically viable
Option 2A has 2 fewer units than 2B
However, 2B has far smaller unit sizes than 2A
  Later, after covering mass balances in depth, we can solve for exact separator and reactor sizes!
An economic analysis is needed to reach the final conclusion, but we’d estimate Option 2B is better!
Which Option is Better?

## Slide 24
L/G Sep. 110˚C
Reactor
F + G → P
I + G → B
20˚C
H2O (1000)
F (aq) [1]
I (aq) [2]
H2O (1000)
F (aq) [1]
I (aq) [2]
L/G Sep.
65˚C
steam
H2O (1000)
F (1)
I (2)
G (excess)
F
G
I
purge
F
G
B
F
G
B
P
P (g)
P (liq) [1]
to market
F
G
B
L/G Sep. ??˚C
B (g)
F (liq)
G (liq)
B (g) [2]
B
L/G Sep. 85˚C
Flow Rates for Option 2B
Considering our conversion rates (independent of ) for each reaction, if 2 mol/min and 1 mol/min react with , then at least 2.9 mol/min must enter our process.
(All flow rates in mol/min)

## Slide 25
By-products may be unavoidable
Reduce unit operation size when applicable
The first design you make may not be (and often isn’t) the best; it may take multiple attempts to find the most optimal
There are A LOT of factors to consider when optimizing a process
Don’t forget to add a purge to a recycle loop!
Takeaways from 2.34