## Slide 1: Exercise 2.35
Original created by Allie Pinterpe ('13), Remastered and reworked by Angela Tang (‘18), Finessed and fine tuned by Francis Ledesma (‘19), Appraised and altered by Michelle Quien (‘20), Scrutinized and streamlined by Drew Lazarow (‘21), Revised and renovated by Sarah Huang and Lucy Cadanau (‘22), Edited and embellished by Ailen Lao and Sanna Vedrine (’23), Trimmed and tidied by Austin Vollweiler (‘24),
Chat GPT'd by Dennis Wu

## Slide 2: Design Goals
Maximize the total value of the product(s)
Minimize the number of units
Minimize the size of each unit

## Slide 3: Design Goals

## Slide 4: Reactions
A
P
Q
X
B
reactor
A
P
Q
A, P, or Q
B or X
B
X
both reactions result in an in equimolar mixture of components
Notes: A reacts reversibly to form P and Q
B reacts reversibly to form X
Since we’re given that A, P, and Q have the same molecular weight and so do B and X, mole balances can be treated as mass balances.
The problem also tells us what happens going into and out of a reactor
If A, P, or Q go in, equalmolar amounts of A, P, and Q come out
Likewise, if B or X go in, equalmolar amounts of B and X come out

## Slide 5: Properties
 | Melting pt (˚C) | Boiling pt (˚C) | Price ($/mol)
A | 51 | 147 | 1
B | 51 | 147 | 20
P | -36 | 77 | 100
Q | 24 | 123 | 30
X | -12 | 95 | 3
A
P
Q
X
B
Notes: Now let’s turn to the physical properties
We can draw temperature lines to see where the phase changes are
Focusing on the first reactions with A, we see that all products are separable. That’s good. But our main design goal is to maximize value, so early we want to focus on producing as much P as possible
Looking at the prices of all given chemicals, P clearly makes the most money, so why not just make P?
We can only get A as a mixture of A and B, and looking at their melting and boiling points, we can’t separate them physically, so we do need to consider chemical reactions of B

## Slide 6: Properties
 | Melting pt (˚C) | Boiling pt (˚C) | Price ($/mol)
A | 51 | 147 | 1
B | 51 | 147 | 20
P | -36 | 77 | 100
Q | 24 | 123 | 30
X | -12 | 95 | 3
A
P
Q
X
B
Notes: Likewise if we focus on the reaction between B and X, we see that they’re separable, but we want to focus on producing as much B as possible
So looking at everything together, we know P and B are the products we want to focus on making and A and B cannot be separated.

## Slide 7: Properties
 | Melting pt (˚C) | Boiling pt (˚C) | Price ($/mol)
A | 51 | 147 | 1
B | 51 | 147 | 20
P | -36 | 77 | 100
Q | 24 | 123 | 30
X | -12 | 95 | 3
A
P
Q
X
B
Notes: Likewise if we focus on the reaction between B and X, we see that they’re separable, but we want to focus on producing as much B as possible
So looking at everything together, we know P and B are the products we want to focus on making and A and B cannot be separated.

## Slide 8: Design Draft 1: single pass
A | (90)
B | (10)
A | (30)
B | (5)
P | (30)
Q | (30)
X | (5)
A | (30)
B | (5)
Q | (30)
Reactor
117 oC
A→A+P+Q
B→B+X
Liquid – Gas Separator
110 oC
P | (30)
X | (5)
110C: separate P,X and A,B,Q
95C: separate P and A,B,Q,X
Notes: We feed our starting materials into a reactor, take the stream that comes out and separate out P, X, and Q.
From the values of the streams coming out of our process, we can calculate the value of our products to be $3915/min
But we need to keep in mind that one of our design goals is to minimize the size of the units. SO WHAT COULD WE DO

## Slide 9: Design Draft 1: single pass
A | (90)
B | (10)
A | (30)
B | (5)
P | (30)
Q | (30)
X | (5)
A | (30)
B | (5)
Q | (30)
Reactor
117 oC
A→A+P+Q
B→B+X
Liquid – Gas Separator
110 oC
P | (30)
X | (5)
P | (30)
A | (30)
B | (5)
X | (5)
Q | (30)
Liquid – Gas Separator
135 oC
Liquid – Gas Separator
85 oC
Notes: We feed our starting materials into a reactor, take the stream that comes out and separate out P, X, and Q.
From the values of the streams coming out of our process, we can calculate the value of our products to be $3915/min
But we need to keep in mind that one of our design goals is to minimize the size of the units. SO WHAT COULD WE DO

## Slide 10: Design Draft 1: single pass
A | (90)
B | (10)
A | (30)
B | (5)
P | (30)
Q | (30)
X | (5)
A | (30)
B | (5)
Q | (30)
Reactor
117 oC
A→A+P+Q
B→B+X
Liquid – Gas Separator
110 oC
P | (30)
X | (5)
P | (30)
A | (30)
B | (5)
X | (5)
Q | (30)
Liquid – Gas Separator
135 oC
Liquid – Gas Separator
85 oC
Product | Flow Rate (mol/min) | Price ($/mol) | Value ($/min)
P | 30 | 100 | 3000
X | 5 | 3 | 15
Q | 30 | 30 | 900
A + B | 35 | 0 | 0
$3915/min total
Are we really maximizing the total value of the products in this process?
Not quite! By adding recycles we can push up the production of of P (= more $$$)
Notes: We feed our starting materials into a reactor, take the stream that comes out and separate out P, X, and Q.
From the values of the streams coming out of our process, we can calculate the value of our products to be $3915/min
But we need to keep in mind that one of our design goals is to minimize the size of the units. SO WHAT COULD WE DO

## Slide 11: How to Improve?
A | (90)
B | (10)
A | (30)
B | (5)
P | (30)
Q | (30)
X | (5)
P | (30)
X | (5)
P | (30)
A | (30)
B | (5)
X | (5)
A | (30)
B | (5)
Q | (30)
Q | (30)
Reactor
117 oC
A→A+P+Q
B→B+X
Liquid – Gas Separator
110oC
Liquid – Gas Separator
135 oC
Liquid – Gas Separator
85 oC
How much money are we making now?
What are the flow rates in the process?
purge
A | (90)
B | (10)
[100]
A | 
B | 

## Slide 12: Iterate to Find Flow Rates at Steady State
[155]
[100]
[65]
A | (90)
B | (10)
A | (30)
B | (5)
P | (30)
Q | (30)
X | (5)
P | (30)
X | (5)
P | (30)
X | (5)
A | (30)
B | (5)
Q | (30)
Q | (30)
Reactor
117 oC
A→A+P+Q
B→B+X
Liquid – Gas Separator
110 oC
Liquid – Gas Separator
135 oC
Liquid – Gas Separator
85 oC
[35]
purge
A | (90)
B | (10)
[100]
A | (30)
B | (5)
[35]
A | (30)
B | (5)
[35]
[135]
[135]
[87.5]
A | (120)
B | (15)
A | (40)
B | (7.5)
P | (40)
Q | (40)
X | (7.5)
 | (40)
 | (7.5)
 | (40)
 | (7.5)
 | (40)
 | (7.5)
 | (40)
 | (40)
[135]
[47.5]
 | (40)
 | (7.5)
[47.5]
A | (40)
B | (7.5)
[47.5]
[147]
[95]
A | (130)
B | (17)
A | (43)
B | (9)
P | (43)
Q | (43)
X | (9)
 | (43)
 | (9)
 | (43)
 | (9)
 | (43)
 | (9)
 | (43)
 | (43)
[147]
[52]
 | (43)
 | (9)
[52]
A | (43)
B | (9)
[52]
[150]
[97]
A | (133)
B | (19)
A | (44)
B | (9)
P | (44)
Q | (44)
X | (9)
 | (44)
 | (9)
 | (44)
 | (9)
 | (44)
 | (9)
 | (44)
 | (44)
[152]
[53]
 | (44)
 | (9)
[53]
A | (44)
B | (9)
[53]
[155]
[100]
A | (134)
B | (20)
A | (45)
B | (10)
P | (45)
Q | (45)
X | (10)
 | (45)
 | (10)
 | (45)
 | (10)
 | (45)
 | (10)
 | (45)
 | (45)
[154]
[55]
 | (45)
 | (10)
[55]
A | (45)
B | (10)
[55]
A | (135)
B | (20)
[100]
Done!
P
X
P
X
Q
A
B
Q
A
B

## Slide 13
Iterating is tedious…

## Slide 14: Instead of Iterating…Work Outside In
A | 
B | 
A | 
B | 
P | 
Q | 
X | 
P | 
X | 
P | 
X | 
A | 
B | 
Q | 
Q | 
Reactor
117 oC
A→A+P+Q
B→B+X
Liquid – Gas Separator
110 oC
Liquid – Gas Separator
135 oC
Liquid – Gas Separator
85 oC
purge
A | (90)
B | (10)
A | 
B | 
A | 
B | 
[155]
[100]
 | (135)
 | (20)
 | (45)
 | (10)
 | (45)
 | (45)
 | (10)
 | (45)
 | (10)
 | (45)
 | (10)
 | (45)
 | (10)
 | (45)
 | (45)
[155]
[55]
 | (45)
 | (10)
[55]
 | (45)
 | (10)
[55]
A  A + P + Q
Ain + Pin + Qin = Aout + Pout + Qout
Pout = Qout
Pout = Qout = Ain / 2 = 45
mass balance
equimolar
solving
mass balance
equimolar
solving
B  B + X
Bin + Xin = Bout + Xout
Bout = Xout
Xout = 10

## Slide 15: Instead of Iterating…Work Outside In
A | 
B | 
A | 
B | 
P | 
Q | 
X | 
P | 
X | 
P | 
X | 
A | 
B | 
Q | 
Q | 
Reactor
117 oC
A→A+P+Q
B→B+X
Liquid – Gas Separator
110 oC
Liquid – Gas Separator
135 oC
Liquid – Gas Separator
85 oC
purge
A | (90)
B | (10)
[100]
A | 
B | 
A | 
B | 
[155]
[100]
 | (135)
 | (20)
 | (45)
 | (10)
 | (45)
 | (45)
 | (10)
 | (45)
 | (10)
 | (45)
 | (10)
 | (45)
 | (10)
 | (45)
 | (45)
[155]
[55]
 | (45)
 | (10)
[55]
 | (45)
 | (10)
[55]
Same result as iterating!
All reaction products leave the system

## Slide 16: Now to evaluate our design
A | 
B | 
A | 
B | 
P | 
Q | 
X | 
P | 
X | 
P | 
X | 
A | 
B | 
Q | 
Q | 
Reactor
117 oC
A→A+P+Q
B→B+X
Liquid – Gas Separator
110 oC
Liquid – Gas Separator
135 oC
Liquid – Gas Separator
85 oC
purge
A | (90)
B | (10)
[100]
A | 
B | 
A | 
B | 
[155]
[100]
A | (135)
B | (20)
A | (45)
B | (10)
P | (45)
Q | (45)
X | (10)
P | (45)
X | (10)
P | (45)
X | (10)
A | (45)
B | (10)
Q | (45)
Q | (45)
[155]
[55]
A | (45)
B | (10)
[55]
A | (45)
B | (10)
[55]
Product | Flow Rate (mol/min) | Price ($/mol) | Value ($/min)
P | 45 | 100 | 4500
X | 10 | 3 | 30
Q | 45 | 30 | 1350
Total: $5880/min
Are we really maximizing the total value of the products in this process?
Notes: Now we’re making more money than before. Look good?

## Slide 17: Let’s go back to see if we’ve met the design goals
Maximize the total value of the product(s)
 | Melting pt (˚C) | Boiling pt (˚C) | Price ($/mol)
A | 51 | 147 | 1
B | 51 | 147 | 20
P | -36 | 77 | 100
Q | 24 | 123 | 30
X | -12 | 95 | 3
Focus on producing the most profitable products: P & B
How do we do this?
Notes: Does our current process satisfy the design goals? Let’s check
Our most important design goal for this exercise is to maximize the value of the products.
Did we do this?

## Slide 18: Design Goals

## Slide 19: Focus on making P & B
A | 
B | 
A | 
B | 
P | 
Q | 
X | 
P | 
X | 
P | 
X | 
A | 
B | 
Q | 
Q | 
Reactor
117 oC
A→A+P+Q
B→B+X
Liquid – Gas Separator
85 oC
Liquid – Gas Separator
110 oC
Liquid – Gas Separator
135 oC
purge
A | (90)
B | (10)
[100]
A | 
B | 
[155]
[100]
A | (135)
B | (20)
A | (45)
B | (10)
P | (45)
Q | (45)
X | (10)
P | (45)
X | (10)
P | (45)
X | (10)
A | (50)
B | (10)
Q | (50)
Q | (45)
[155]
[55]
A | (50)
B | (10)
[60]
A | (50)
B | (10)
[60]
Recycling Q will help us produce more P!
Notes: Recycle Q back into the process to produce more P

## Slide 20: Focus on making P & B
A | 
B | 
A | 
B | 
P | 
Q | 
X | 
P | 
X | 
P | 
X | 
A | 
B | 
Q | 
Reactor
117 oC
A→A+P+Q
B→B+X
Liquid – Gas Separator
85 oC
Liquid – Gas Separator
135 oC
A | (90)
B | (10)
[100]
purge
A | (180)
B | (20)
Q | (90)
A | (90)
B | (10)
P | (90)
Q | (90)
X | (10)
P | (90)
X | (10)
P | (90)
A | (90)
B | (10)
Q | (90)
[290]
[290]
[190]
[100]
A | (90)
B | (10)
Q | (90)
[190]
Are we really maximizing the total value of the products in this process?
While we are now maximizing the value of P produced….
…we can still make more money by converting X to B
X | (10)
Notes: Do mass balances the outside in way

## Slide 21: Focus on making P & B
A | (180)
B | (20)
Q | (90)
A | (90)
B | (10)
P | (90)
Q | (90)
X | (10)
P | (90)
X | (10)
P | (90)
X | (10)
A | (90)
B | (10)
Q | (90)
Reactor
117 oC
A→A+P+Q
B→B+X
Liquid – Gas Separator
110 oC
Liquid – Gas Separator
135 oC
purge
A | (90)
B | (10)
[100]
[290]
[290]
[190]
[100]
A | (90)
B | (10)
Q | (90)
[190]
✓
Reactor
117 oC
X→B+X
Liquid – Gas Separator
117 oC
B | 
X | 
purge
B | 
X | 
X | 
X | 
B | (10)
B | (10)
X | (10)
X | (10)
X | (10)
X | (20)
Product | Flow Rate (mol/min) | Price ($/mol) | Value ($/min)
P | 90 | 100 | 9000
B | 10 | 20 | 200
Total: $9200/min
✓
Notes: Recycle X back to make B

## Slide 22: Chemical Process Recap
Made a design that worked to isolate and maximize P and B
Recycled unused reactants to increase product yield
Utilized a second reactor to convert a less favorable product to a more favorable one

## Slide 23: Our Process Recap (Takeaways)
Check & prioritize your design goals
  May need to change design multiple times to make sure your top goal is accomplished!
Recycle Loops
  Remember to purge
  Use to increase output of certain products
  Calculate flow rates by
    Iterating until numbers converge
    System mass balance, working outside in
One input and one output stream per reactor

## Slide 24
Calculation Session 3
Homework questions? Ask!
Exercises 3.4, 3.10, and 3.24 – formal mass balances.
1. Draw system borders.
2. Describe system and state assumptions
or write rate in = rate out
Exercise 2.35 – process design with informal, approximate flow rates.
Assess your process:
Does your process agree with an overall mass balance?
Given Ain = 90  (A + P + Q)out = ?
Given Bin = 10  (B + X)out = ?
Does your process achieve the maximum P output?