## Slide 1: Exercise 3.10
Created by: Jiamin Zhang ’16 and Maxine Chan ‘16
Revised by:
Amy Penick ’17
Anderson Luke ‘18
Joe Hassler ’18
Rose Yin ’19
Kasim Khan ’20
Tommy Bradford ’21
Lucy Cadanau ’22
Ariel Struzyk ’23
Burke Combs ’24
Donovan Cho ‘25
Mass Balances
(and the power of colorful system borders)

## Slide 2: Part (A): What is the flow rate of Stream 2?
rate in = rate out
FT,2 = ?
Fresh OJ
80. wt% water
377 kg/min
Concentrated OJ
20. wt% water
Steam
liquid-gas separator
100 °C
1
2
3
Notes: (A) Calculate flow rate of stream 2 from evaporator

## Slide 3
liquid-gas separator
100 °C
1
2
3
Let W = water
Let Z = nonwater component (orange zest)
Let T = total (water and zest)
Flow in = Flow out (Assume no chemical reaction and SS)
Do a total mass balance around the liquid-gas separator:
FT,in = FT,out
FT,1 = FT,2 + FT,3
377 kg/min = FT,2 + FT,3
FT,2 = 377 - FT,3
FT,2 = 377 – 94.25
FT,2 = 282.75 kg/min
FT,2 = 280 kg/min
Do a mass balance on Z around the liquid-gas separator:
FZ,in = FZ,out
FZ,1 = FZ,2 + FZ,3
xZ,1FT,1 = xZ,3FT,3
(.20)(377) = (.80)FT,3
FT,3 = 94.25 kg/min
Fresh OJ:
80. wt% water
377 kg/min
Concentrated OJ:
20. wt% water
Steam
Goal
Sig figs!
Find separately!
Zero!
Solve the system
Notes: The method shown on this slide involves balancing water throughout the system, since we are finding the water present in Stream 2.
However, it is easier to do a balance on Z, since one can simply subtract FT,3 (94.3 kg/min) from FT,1 to obtain FT,2 as 280 kg/min.
Note: “Then, we replace the water flow rates with the total flow rates multiplied by that stream’s respective mass fraction of water”

## Slide 4: Part (B): A little more intimidating…
Concentrated orange juice
5.0 wt% water
evaporator
1
3
4
5
6
liquid-gas separator
100 °C
2
rate in = rate out
FT,2 = ?
We’ve already done this!
FT,2 = 280 kg/min
Steam
Concentrated OJ
20. wt% water
Fresh OJ
80. wt% water
377 kg/min
Notes: Goal for (B): Calculate the flow rate of steam in Stream 2
Even though this diagram is more intimidating, the answer for (B) is actually the same as for (A), because you can draw the same border for your mass balance!

## Slide 5: Part (C): 5% “zest” bypasses evaporator
Fresh OJ
80. wt% water
377 kg/min
liquid-gas separator
100 °C
1
3
4
5
6
2
FT,4 = ?
FT,5 = ?
(i.e. 5% of the zest that enters goes through Stream 5, NOT Stream 4)
Steam
Concentrated OJ
20. wt% water
Concentrated OJ
5.0 wt% water
Fresh OJ
80. wt% water
Fresh OJ
80. wt% water
Splitters do NOT change composition!
Notes: Goal for (C): calculate the flow rates for streams 4 & 5

## Slide 6
liquid-gas separator
100 °C
1
3
4
5
6
2
5.0 wt% of the Zest in Stream 1 goes through the bypass stream (Stream 5)
Write an equation from the problem statement
FZ,5 = 0.05* FZ,1 = 0.05*xZ,1*FT,1
FZ,5 = .05(.20* 377)
FZ,5 = 3.77 kg/min
Calculate FT,5 from FZ,5
xZ,5 * FT,5 = FZ,5
FT,5 = FZ,5 / xZ,5 = 3.77 / 0.20 = 18.85
FT,5 = 19 kg/min
To calculate FT,4 , do a total balance around the splitter
FT,1 = FT,4 + FT,5
377 = 19 + FT,4
FT,4 = 360 kg/min
Fresh OJ:
80. wt% W
377 kg/min
5.0 wt% water
20 wt% W
94.3 kg/min
Steam
280 kg/min
80. wt% W
80. wt% W
Solve the system
Notes: Clarify: 5. wt% of the O in (3) comes from bypass stream (5)
FT,3 was calculated in part (A).
In this method, we first derive the amount of zest in stream 5 from the problem statement. We use that to calculate the amount of zest in stream 4. We then use a mass balance around the separator, and the consistent percent compositions, to back-calculate the total flow rates of each.

## Slide 7
liquid-gas separator
100 °C
1
3
4
5
6
2
5.0 wt% of the Zest in Stream 1 goes through the bypass stream (Stream 5)
Write an equation from the problem statement
FZ,5 = .05* FZ,1 = .05 * FZ,3
FZ,5 = .05(.80*FT,3)
FZ,5 = .05(.80)(94.3) = 3.77 kg/min
Do a balance on Z around the splitter:
FZ,1 = FZ,4 + FZ,5
(.20)*377 = FZ,4 + 3.77
FZ,4 = 71.6 kg/min
Calculate FT,4 from FZ,4
(0.20)FT,4 = FZ,4
FT,4 = 358 kg/min ≈ 360 kg/min
To calculate FT,5 , do a total balance around the splitter:
FT,1 = FT,4 + FT,5
377 = 358 + FT,5
FT,5 = 19 kg/min
Fresh OJ:
80. wt% W
377 kg/min
5 wt% water
20 wt% W
94.3 kg/min
Steam
280 kg/min
80. wt% W
80. wt% W
Instead of calculating FT,5, you can calculate FZ,4 instead…
Alternatively…
Sig figs!
Notes: Clarify: 5. wt% of the O in (3) comes from bypass stream (5)
FT,3 was calculated in part (A).
In this method, we first derive the amount of zest in stream 5 from the problem statement. We use that to calculate the amount of zest in stream 4. We then use a mass balance around the separator, and the consistent percent compositions, to back-calculate the total flow rates of each.

## Slide 8
Steady State + No Reaction in = out
Splitters maintain composition
Draw system borders that save work – you can potentially ignore some internal streams!
Remember sig-figs!
There are multiple ways to solve a problem
Don’t forget your Vitamin C
3.10: Takeaways
Notes: Conservation of mass
No need to worry about recycle loop, draw system boundary to include both units