## Slide 1: Exercise 3.24
Created by Jiamin Zhang ’16 and Maxine Chan ’16 Revised by Amy Penick ’17, Anderson Luke ‘18, Joe Hassler ’18, Max Serota ’22, Sanna Vedrine ‘23, Ailen Lao ’23, Austin Kwan ’24, Lauren de Silva ‘25
Notes: Extraction of oil from soybeans

## Slide 2
Oil
Extractor
Oil
Recovery
Soybeans:
37 wt% Oil
45 wt% Protein
18 wt% Fiber
2.3 kg/min
1
2
5
3
4
6
Protein
Fiber
3.0 wt% Hexane
Hexane
Oil
Hexane
7.4 kg/min
Hexane
Oil
Nomenclature:
FT,n = Total flow rate of stream n
xP,n= mass fraction of Protein in stream n
Notes: Calculate the flow rate and composition of stream 2
Use O,P,F to represent oil, protein, and fiber, respectively

## Slide 3
Oil
Extractor
Oil
Recovery
37 wt% O
45 wt% P
18 wt% F
2.3 kg/min
1
2
5
3
4
6
P
F
3.0 wt% H
H
O
H
7.4 kg/min
H
O
Part (A)
What is FT,2 and its composition?
Notes: In Part A, we need the flow rate and composition of stream 2.
Where should we draw the system borders?
Draw border around oil extractor, or whole system. Either one works.

## Slide 4
Total in = Total Out
Pin = Pout
Oil
Extractor
Oil
Recovery
37 wt% O
45 wt% P
18 wt% F
2.3 kg/min
1
2
5
3
4
6
P
F
3.0 wt% H
H
O
H
7.4 kg/min
H
O
Fin = Fout
1. Let’s define our system
Notes: Protein and fiber only come into the system and exit in one stream: could be easy to work with.
Overall mass balance? [pause]
Total In = Total Out
No
Species balance on Protein and Fiber

## Slide 5
Protein in= Protein out
FP,1 + FP,5 = FP,2 + FP,6
FP,1 = xP,1FT,1 = 0.45(2.3 kg/min)
= 1.035 kg/min
FP,2 = 1.035 kg/min
Fiber in = Fiber out
FF,1 + FF,5 = FF,2 + FF,6
FF,1 = xF,1FT,1 = 0.18(2.3 kg/min)
= 0.414 kg/min
FF,2 = 0.414 kg/min
Assume protein is conserved
Assume fiber is conserved.
37 wt% O
45 wt% P
18 wt% F
2.3 kg/min
P
F
3.0 wt% H
1.035 kg/min P
0.414 kg/min F
3.0 wt% H
1
2
3
4
5
6
Note:
There is NO protein or fiber in input stream 5 or output stream 6.
xP,5 , xP,6 = 0
xF,5 , xF,6 = 0

## Slide 6
1.035 kg/min P
0.414 kg/min F
3.0 wt% H
FT,2 = FP,2 + FF,2 + FH,2
FH,2 = 0.030 FT,2
FT,2 = (1.035 + 0.414) kg/min + 0.030 FT,2
(1 - 0.030) FT,2 = (1.035 + 0.414) kg/min
FT,2 = 1.5 kg/min
Composition?
37 wt% O
45 wt% P
18 wt% F
2.3 kg/min
1
2
3
4
5
6

## Slide 7
Oil
Extractor
Oil
Recovery
37 wt% O
45 wt% P
18 wt% F
2.3 kg/min
1
2
5
3
4
6
69 wt% P
28 wt% F
3.0 wt% H
1.5 kg/min
H
O
H
7.4 kg/min
H
O
Parts (B) & (C)
FT,6 ? FT,5 ?
Notes: Hexane and Oil only come into the system and exit in one stream: could be easy to work with.
System borders?? [PAUSE]

## Slide 8
FO,in = FO,out
FO,1 = FO,6
FT,6 = FO,6
FT,6 = xO,1FT,1
FT,6 = 0.37*2.3 kg/min
FT,6 = 0.85 kg/min
Conservation of Oil
B.
37 wt% O
45 wt% P
18 wt% F
2.3 kg/min
1
2
3
4
5
6
O
1.035 kg/min P
0.414 kg/min F
3.0 wt% H
H
Note:
There is NO oil in input stream 5 or output stream 2.
xO,5 , xO,2 = 0
Notes: NOTE: One more sig fig can be achieved by using the unrounded values of the flow rates. The more accurate result is 0.045 kg/min, which can be calculated using the total mass or with a mass balance on hexane.

## Slide 9
FH,in = FH,out
FH,5 = FH,2
FT,5 = FH,5
FT,5 = 0.03FT,2
FT,5 = 0.03*1.5 kg/min
FT,5 = 0.05 kg/min
Conservation of Hexane
C.
37 wt% O
45 wt% P
18 wt% F
2.3 kg/min
1
2
3
4
5
6
O
1.035 kg/min P
0.414 kg/min F
3.0 wt% H
1.5 kg/min
H
Note:
There is NO Hexane in input stream 1 or output stream 6.
xH,1 , xH,6 = 0
Notes: NOTE: One more sig fig can be achieved by using the unrounded values of the flow rates. The more accurate result is 0.045 kg/min, which can be calculated using the total mass or with a mass balance on hexane.

## Slide 10
Check our Answer!
Conservation of mass
FT,in = FT,out
FT,1 + FT,5 = FT,2 + FT,6
2.3 + 0.05 = 1.5 + 0.85
2.35 kg/min = 2.35 kg/min
2.3 kg/min
1
2
3
4
5
6
0.85 kg/min
1.5 kg/min
0.05 kg/min
Notes: NOTE: One more sig fig can be achieved by using the unrounded values of the flow rates. The more accurate result is 0.045 kg/min, which can be calculated using the total mass or with a mass balance on hexane.

## Slide 11: Takeaways
Steady State + No Reaction Rate in = Rate out
  No Accumulation
Draw system borders (that simplify your analysis)
Include UNITS (always)
Check your work with an alternative method
Notes: Conservation of mass
No need to worry about recycle loop, draw system boundary to include both units