## Slide 1
Created by Lauren Taylor ‘14
Edited by Katrina Curtiss ’15, McKenzie Hubert ’16, Aron Coraor ’17, Ameer Basrai ’18, Francis Ledesma ’19. Michelle Quien ’20, Andrew Simon ’21, Kelsey Levine ’22, Ailen Lao and Sanna Vedrine ’23, Maggie MacNeel ’24, Lauren de Silva and Dennis Wu ‘25
Design Exercise
Design Exercise 3.116
??
Notes: sanna

## Slide 2: Design Goals
1. Maximize $$$$ from selling pure products
2. Minimize the number of units
3. Minimize the size of each unit
Notes: sanna

## Slide 3: Design Considerations
Reactor
Type 1
37 °C
A (2)
A (1)
P (1)
Aout = ½ Ain
Pout = Pin + ½ Ain
Notes: ailen
Type 1 Reactor
  Converts ½ of A to P

## Slide 4
Reactor
Type 2
85 °C
A (5)
P (4)
Q (1)
Pout = 4 Qout
Pout = Pin + 4/5 Ain
Qout = Qin + 1/5 Ain
Design Considerations
Notes: ailen
Type 2 Reactor
  Converts 100% of A to P and Q in a ratio of 4:1 (P:Q)

## Slide 5
Reactor
Type 3
49 °C
A (9)
B (2)
P (6)
Z (2)
P (7)
Z (4)
A (8)
Pout = Pin + 1/9 Ain
Zout = Zin + Bin
Design Considerations
Notes: ailen
Type 3 Reactor
  Converts 1/9 A to P
  Converts 100% B to Z

## Slide 6
 | M.W. | Melting Pt, °C | Boiling Pt, °C | Price ($/mol) | Notes
A | 120 | -3 | 122 | 100 | Must not be heated above 250 °C
B | 133 | -3 | 122 | 35 | 
P | 120 | -3 | 122 | 1000 | 
Q | 120 | 18 | 147 | 20 | Suspected carcinogen
Z | 133 | -28 | 95 | 10 | Non-toxic
Get pure P by completely reacting A and B
Design Considerations
Notes: ailen

## Slide 7: Design Considerations
Only use 1 of each reactor type
All reactions are irreversible
Start with 100 mol/hr of 90% A and 10% B
HINT: It is possible to produce P in 100% purity, with less than 1% of A converted to Q
  This means we can obtain < 0.9 mol Q
Notes: ailen

## Slide 8: Outline Initial Game Plan
Reactor
Type 1
37 °C
A (2)
A (1)
P (1)
Reactor
Type 2
85 °C
A (5)
Q (1)
P (4)
Reactor
Type 3
49 °C
A (9)
B (2)
P (6)
Z (2)
P (7)
Z (4)
A (8)
Benefit
Produces only P, but low conversion rate
Separates A from P by producing Q
Separates B from P by producing Z
Reactor
Notes: sanna

## Slide 9
A (90)
B (10)
Reactor
Type 3
49 °C
A (80)
P (10)
Z (10)
Liquid-Gas Separator
110 °C
Z (10)
A (80)
P (10)
Q (16)
P (74)
Q (16)
Reactor
Type 2
85 °C
Liquid-Gas Separator
135 °C
P (74)
Revenue: $74,420/hour
Since we want to minimize unit sizes,
let’s get rid of B first
Initial Game Plan
Use Type 3 to create Z from B
Use Type 2 to remove A and produce P&Q
Separate Q and P to sell
Notes: sanna

## Slide 10
What needs improvement
How to improve
What I like
1. Removed B early and reduced the size of later units
2. Produced pure P by using reactor 2
Produce a lot of Q
2. Can produce more P
Problem: Produce less Q
Solution: React less A
Post-Design Analysis

## Slide 11: Post-Design Analysis
Initial designs are seldom perfect…
Design Goals:
Maximize revenue
Minimize # units
Minimize size of units
Need to increase the yield of P!
Notes: sanna + ailen

## Slide 12: Outline Initial Game Plan
Reactor
Type 1
37 °C
A (2)
A (1)
P (1)
Reactor
Type 2
85 °C
A (5)
Q (1)
P (4)
Reactor
Type 3
49 °C
A (9)
B (2)
P (6)
Z (2)
P (7)
Z (4)
A (8)
Benefit
Produces only P, but low conversion rate
Separates A from P by producing Q
Separates B from P by producing Z
Reactor
Notes: sanna

## Slide 13
A (90)
B (10)
Reactor
Type 3
49 °C
A (80)
P (10)
Z (10)
Liquid-Gas Separator
110 °C
Z (10)
A (80)
P (10)
Reactor
Type 1
85 °C
Q (8)
P (82)
Q (8)
Reactor
Type 2
85 °C
Liquid-Gas Separator
135 °C
P (82)
A (40)
P (50)
Where should we put the Type 1 reactor?
To minimize how much Q is made,
let’s use a Type 1 reactor to remove some A before reactor 2
Revenue: $82,260/hour
A (80)
P (10)
Q (16)
P (74)
Q (16)
Reactor
Type 2
85 °C
Liquid-Gas Separator
135 °C
P (74)
We still haven’t maximized the amount of P or our profit!
<1% A converted into Q, which is 0.9 mol
Notes: ailen

## Slide 14: How do we convert more A?
2 Major Options:
    Add another reactor
    Add a recycle
Prompt prohibits any more reactors, so let’s design a recycle
Notes: ailen

## Slide 15
A (90)
B (10)
Reactor
Type 3
49 °C
A (80)
P (10)
Z (10)
Liquid-Gas Separator
110 °C
Z (10)
A (80)
P (10)
Reactor
Type 1
85 °C
Q
P
Q
Reactor
Type 2
85 °C
Liquid-Gas Separator
135 °C
P
A
P
A
P
A
P
A
P
Informal System Mass Balances!
What about impurities?
purge
Notes: ailen
since flow rates are 1 sig fig
we know we have 90 mol A , therefore p + q = a in
smallest amount of Q = 1

## Slide 16
A (90)
P
Z (10)
Q
B (10)
Design hint tells us our target Qout ≈ 1 mol/hour
Ain= Aout + Pout+ Qout
90 = 0 + Pout + 1
Pout ≈ 89 mol/hour
(1)

## Slide 17
A (90)
B (10)
Reactor
Type 3
49 °C
A (80)
P (10)
Z (10)
Liquid-Gas Separator
110 °C
Z (10)
A (80)
P (10)
Reactor
Type 1
85 °C
Q
P
Q
Reactor
Type 2
85 °C
Liquid-Gas Separator
135 °C
P
A
P
A
P
A
P
A
P
(1)
(1)
(89)
(89)
purge
Notes: ailen
since flow rates are 1 sig fig
we know we have 90 mol A , therefore p + q = a in
smallest amount of Q = 1

## Slide 18
P (89)
A
P
Reaction:
A  P + Q
100% conversion
4P:1Q
Q (1)
Solve for the amount of A coming in
Qout = Ain
1mol/hr = Ain
Ain = 5 mol/hr
Solve for the amount of P coming in:
Pout = Pin + Ain
89 mol/hr = Pin + 4 mol/hr
Pin= 85 mol/hr
(5)
(85)

## Slide 19
A (90)
B (10)
Reactor
Type 3
49 °C
A (80)
P (10)
Z (10)
Liquid-Gas Separator
110 °C
Z (10)
A (80)
P (10)
Reactor
Type 1
85 °C
Q
P
Q
Reactor
Type 2
85 °C
Liquid-Gas Separator
135 °C
P
A
P
A
P
A
P
A
P
(85)
(1)
(1)
(89)
(5)
(89)
purge
Notes: ailen
since flow rates are 1 sig fig
we know we have 90 mol A , therefore p + q = a in
smallest amount of Q = 1

## Slide 20
A (90)
B (10)
Reactor
Type 3
49 °C
A (80)
P (10)
Z (10)
Liquid-Gas Separator
110 °C
Z (10)
Reactor
Type 1
85 °C
Q
P
Q
Reactor
Type 2
85 °C
Liquid-Gas Separator
135 °C
P
A
P
A
P
A
P
A
P
(85)
(1)
(1)
(89)
(5)
Reactor 1 converts ½ of A to P,
75*2 = 150 mole/hr
(150)
(75)
(89)
purge
A (80)
P (10)
Notes: sanna

## Slide 21
A (90)
B (10)
Reactor
Type 3
49 °C
A (80)
P (10)
Z (10)
Liquid-Gas Separator
110 °C
Z (10)
Reactor
Type 1
85 °C
Q
P
Q
Reactor
Type 2
85 °C
Liquid-Gas Separator
135 °C
P
A
P
A
P
A
P
A
P
(85)
(1)
(1)
(89)
(5)
(89)
purge
A (80)
P (10)
Notes: sanna

## Slide 22
A (80)
P (10)
A (5)
P (85)
Reaction:
A  P
50% conversion
Lets find how much A is consumed in our process:
Aconsumed = Ain – Aout
Aconsumed= 80 mol/hr – 5 mol/hr
Aconsumed = 75mol/hr
Reactor
Type 1
85 °C
A
P
A
P
A (75)
50% of A is consumed…
Thus, we must start with 2x75=150 mol/hr A
(150)
(75)

## Slide 23
A (90)
B (10)
Reactor
Type 3
49 °C
A (80)
P (10)
Z (10)
Liquid-Gas Separator
110 °C
Z (10)
A (80)
P (10)
c
Reactor
Type 1
85 °C
Q
P
Q
Reactor
Type 2
85 °C
Liquid-Gas Separator
135 °C
P
A
P
A
P
A
P
A
P
(85)
(1)
(1)
(89)
(5)
Stream compositions don’t change from splitter
=1275
(150)
(75)
(1275)
(89)
purge
Notes: sanna

## Slide 24
A (90)
B (10)
Reactor
Type 3
49 °C
A (80)
P (10)
Z (10)
Liquid-Gas Separator
110 °C
Z (10)
A (80)
P (10)
Reactor
Type 1
85 °C
Q
P
Q
Reactor
Type 2
85 °C
Liquid-Gas Separator
135 °C
P
A
P
A
P
A
P
A
P
(85)
(1)
(1)
(89)
(5)
A1 = A2 + A3
A3 = 75 – 5 = 70
(150)
(75)
(1275)
(1200)
(70)
(1190)
(89)
P1 = P2 + P3
P3 = 1275 – 85 = 1190
2
1
3
purge
Notes: sanna

## Slide 25
A (90)
B (10)
Reactor
Type 3
49 °C
A (80)
P (10)
Z (10)
Liquid-Gas Separator
110 °C
Z (10)
A (80)
P (10)
Reactor
Type 1
85 °C
Q
P
Q
Reactor
Type 2
85 °C
Liquid-Gas Separator
135 °C
P
A
P
A
P
A
P
A
P
(85)
(1)
(1)
(89)
(5)
Alternatively….
Try a deductive method.
(89)
(x)
(y)
(.5x)
(y+.5x)
x-80 = (.5x-5)
y-10 = (y+.5x-85)
purge
Notes: ailen

## Slide 26
Y = 1200
X = 150

## Slide 27
A (90)
B (10)
Reactor
Type 3
49 °C
A (80)
P (10)
Z (10)
Liquid-Gas Separator
110 °C
Z (10)
A (80)
P (10)
Reactor
Type 1
85 °C
Q
P
Q
Reactor
Type 2
85 °C
Liquid-Gas Separator
135 °C
P
A
P
A
P
A
P
A
P
(85)
(1)
(1)
(89)
(5)
(150)
(75)
(1275)
(1200)
(70)
(1190)
(89)
Revenue: $89,120/hour
purge
yay!
Notes: ailen

## Slide 28: Post-Design Analysis
Design Goals:
Maximize revenue
Minimize # units
Minimize size of units
Future improvements
Produce even more P by reducing Q
Notes: sanna + ailen

## Slide 29
A (90)
B (10)
Reactor
Type 3
49 °C
A (80)
P (10)
Z (10)
Liquid-Gas Separator
110 °C
Z (10)
A (80)
P (10)
Reactor
Type 1
85 °C
Q
P
Q
Reactor
Type 2
85 °C
Liquid-Gas Separator
135 °C
P
A
P
A
P
A
P
A
P
(87.5)
(.5)
(.5)
(89.5)
(2.5)
(155)
(77.5)
(2710)
(2632.5)
(75)
(2622.5)
(89.5)
What if Qout=0.5?
The recycle more than doubles!
purge
Notes: sanna
By producing 0.5 more mol of P, we have to recycle 1000 more mols of P, which makes the reactor HUGE and not worth it!

## Slide 30: Key Takeaways
Work backwards to find relative flow rates
  Determine reactor generation and consumption in the recycle loop
  Ratios and mass balances across splitters/combiners
  Inductive vs. Deductive methods
The more P we want to produce, the more that needs to be recycled!
Notes: ailen