## Slide 1
Created by: Parry Grewal (‘10)
Modified by: Christine Catudal (‘11)
Yuan Li (‘12)
Samantha Tierney (‘13)
Alana Szkodny (‘14)
Kathy Fein (‘15)
Jesse Garcia (‘16)
Robert Lee (‘17)
Ameer Basrai (‘18)
Olivia Young (‘19)
Spencer Hong (‘20)
Emily Spiek (‘21)
Max Serota (‘22) / Lucy Cadanou (‘22)
Leon Lee (‘23)
Burke Combs (‘24)
Dennis Wu (‘25)
Lara Capellino (‘26)
Exercise 3.64
**Heat Exchange Flow**
Yo, in the lab, where the numbers rise,
Chemical engineers, we’re the wise guys.
Heat exchangers work, let the energy mix,
Pipes and plates, yo, it’s all in the fix.
We calculate flows, plot it on the graph,
Turning up the heat, let the process laugh.
From chill to thrill, we shift the game,
Efficiency’s our goal, and we’re bringing the flame.
We got copper and steel, crafting with style,
Transforming the heat, making it worthwhile.
In the heartbeat of industry, we take our stance,
From the lab to the field, watch us advance!
So here’s to the engineers, we’re making it right,
In the world of heat exchange, we ignite the night.
With every exchange, we rise and we flow,
Chemical kings and queens, let the knowledge grow!
-ChatGPT

## Slide 2
Heated
Evaporated
FT, 2 = ?
FT, 3 = ?
4,500 kJ/min
Getting Started

## Slide 3: Rules for Energy Balances
We cannot calculate the absolute energy of a mass stream (do NOT state q1 = 100 kJ/min). We must calculate the change (q1 – q0) instead.
We cannot measure energy (q). We must measure a change in temperature, phase, etc. and use thermodynamics to calculate energy.

## Slide 4
Complete Energy Balance
Equivalent Units
Two Solution Methods

## Slide 5
Energy Balance on Entire Process:
Rate of energy in = Rate of energy out
Mass Balance on Entire Process:
Flow rate of mass in = Flow rate of mass out
Two equations, two unknowns!
Wait! I thought you said we couldn’t calculate absolute q’s!
Method 1: Balances on Entire Process
We need another equation…

## Slide 6
Our energy balance appears to violate our rule that “we cannot calculate the energy of a mass stream”
But, with some rearrangement, we are calculating differences
Stream 2 Flow Rate = 1.3 kg/min
Stream 3 Flow Rate = 6.0 kg/min
Method 1: Balances on Entire Process

## Slide 7
Note:
- All water is heated to 100ºC
- Some water is then evaporated to steam, but still is at 100ºC
3
Method 2: Equivalent Units
2
1

## Slide 8
Elementary Energy Units!
What is an elementary energy unit?
1 mass stream in, 1 mass stream out; 1 energy change.
All mass passing through the units is heated or changes phase.
Method 2: How to show steps in diagram?

## Slide 9
Calculate qwarmer:
1a
2
3
1
water at 100.ºC
steam at 100.ºC
7.3 kg/min
water
50.ºC
evaporator
q
heater
= 4500 kJ/min
1b
q
evap
q
warmer
warmer
water
100.ºC
equivalent boiler
Method 2: Find qwarmer

## Slide 10
1a
2
3
1
water at 100.ºC
steam at 100.ºC
7.3 kg/min
water
50.ºC
evaporator
q
heater
= 4500 kJ/min
1b
q
evap
q
warmer
warmer
water
100.ºC
equivalent boiler
= 1520 kJ/min
Use an energy balance on the splitter:
Method 2: Find qevap

## Slide 11
1a
2
3
1
water at 100.ºC
steam at 100.ºC
7.3 kg/min
water
50.ºC
evaporator
q
heater
= 4500 kJ/min
1b
q
evap
q
warmer
warmer
water
100.ºC
equivalent boiler
= 1520 kJ/min
= 2980 kJ/min
How much steam can be produced by qevap?
Method 2: Find FT,2

## Slide 12
Stream 2 Flow Rate = 1.3 kg/min
Stream 3 Flow Rate = 6.0 kg/min
1a
2
3
1
water at 100.ºC
steam at 100.ºC
7.3 kg/min
water
50.ºC
evaporator
q
heater
= 4500 kJ/min
1b
q
evap
q
warmer
warmer
water
100.ºC
equivalent boiler
= 1520 kJ/min
= 2980 kJ/min
1.3 kg/min
We can use a mass balance on the entire process to get FT,3:
6.0 kg/min
Method 2: Find FT,3

## Slide 13
2 unknowns
Need 2 equations
      Energy Balance
      Mass Balance
 Solve
Review: Method 1

## Slide 14
1a
2
3
1
water at 100.°C, 6.0 kg/min
steam at 100. °C, 1.3 kg/min
7.3 kg/min
water
50.°C
evaporator
q
heater
= 4500 kJ/min
1b
q
evap
q
warmer
warmer
water
100.°C
equivalent boiler
= 1520 kJ/min
= 2980 kJ/min
Steps
1. Calculate qwarmer
2. Use qwarmer to calculate qevap
3. Determine how much water can be converted into steam (at 100.°C) by qevap  FT,2
4. Calculate FT,3 by mass balance
Simple mass units can be complex energy units – break it up
Review: Method 2

## Slide 15
There are multiple valid approaches to solving a problem while getting the same answer.
We can use the method of equivalent energy units to organize our calculations.
3.64: Key Takeaways