## Slide 1: Exercise 3.66
Created by McKenzie Hubert ('16) & Maxine Chan ('16)
Revised by Jenny Bushnell (‘17), Angela Tang (‘18), Sydney Brannan (‘19), Michelle Quien (‘20), Ann Metzloff (‘21), Sarah Huang (‘22), Leon Lee (‘23), Austin Vollweiler (24’), Donovan Cho (‘25)

## Slide 2: Overview
1
2
3
4
Mixer
Water at 16°C
10. kg/min
Ice at -12°C
4.0 kg/min
Steam at 215°C
6.0 kg/min
Find:
FT,4
T4
Composition

## Slide 3: FT,4 – Mass Balance
1
2
3
4
Mixer
Water at 16°C
10. kg/min
Ice at -12°C
4.0 kg/min
Steam at 215°C
6.0 kg/min
Rate in = Rate out
No chemical rxns
FT,1 + FT, 2 + FT, 3 = FT,4
10. + 4.0 + 6.0 = FT,4
FT,4 = 20. kg/min

## Slide 4: Temperature and Composition
Process with 3 inputs: water, ice, steam
What are possible combinations leaving?
  All steam
  Water + steam
  All water
  Water + ice
  All ice
Thermodynamic properties for H2O |  | 
 | P = 1 atm | P = 0.005 atm
(joules °C-1 mol-1)* | 33. (solid) | 33. (solid)
 | 75. (liquid) | 75. (liquid)
 | 35. (vapor) | 33. (vapor)
boiling point (°C) | 100 | -2
melting point (°C) | 0 | -2
heat of vaporization (joules mol-1) | 4.1 × 104 | 4.5 × 104
heat of melting (joules mol-1) | 6.0 × 103 | 6.8 × 103
* varies with temperature. These values are valid to two significant figures in the range –50°C to 200°C. |  | 
Energy is conserved in the mixer!
Notes: First going to assume that it’s only water coming out

## Slide 5: Again, Our Process
Water at 16°C
10. kg/min
Ice at -12°C
4.0 kg/min
Mixer
3
Steam at 215°C
6.0 kg/min
4
Assume
Water at ?? °C
20. kg/min
1
2

## Slide 6
Warmer
1
2
3
Water at 16°C
10. kg/min
Ice at -12°C
4.0 kg/min
Steam at 215°C
6.0 kg/min
Cooler
Warmer
Condenser
2a
3a
Water at 0°C
Water at 0°C
Water at 0°C
qcooler
qwarmer+melter
qcondendser+cooler
qtotal
4
Water at ?? °C
20. kg/min
1a
equivalent mixer
Melter
Cooler
3b
Cooler
No external heat input
Warm/cool each stream to 0C water, then warm up to final temperature
Notes: Look at warmer+melter first

## Slide 7: Warmer + Melter
2
Ice at -12°C
4.0 kg/min
Warmer
2a
qwarmer+melter
Melter
Notes: Δ

## Slide 8: Repeat Analysis for Other Streams
Condenser + Cooler
Cool steam to 100°C
Condense steam to water
Cool water from 100°C to 0°C

## Slide 9: Repeat Analysis for Other Streams
Cooler
1) Cool water from 16°C to 0°C

## Slide 10
Warmer
1
2
3
Water at 16°C
10. kg/min
Ice at -12°C
4.0 kg/min
Steam at 215°C
6.0 kg/min
Cooler
Warmer
Condenser
2a
3a
Water at 0°C
Water at 0°C
Water at 0°C
qcooler
qwarmer+melter
qcondendser+cooler
qtotal
4
Water at ?? °C
20. kg/min
1a
equivalent mixer
Melter
Cooler
3b
Cooler

## Slide 11: Determine Exit Temperature
Balance around Combiner
rate of energy in = rate of energy out
qcooler + qcondenser+cooler = qtotal + qwarmer+melter
qtotal = +16,756 kJ/min
Balance around Warmer
rate of energy in = rate of energy out
qtotal = q4 – q3 = FT,4CP,water(T4 – T3a)
T4 = 201°C
BUT WAIT!
H2O isn’t liquid at 201°C!
Let’s check our assumptions…
qcondenser+cooler
qcooler
qwarmer+melter
qtotal
warmer
3a
4
qtotal
Water at ?? °C
20. kg/min

## Slide 12
What are possible combinations leaving?
  All ice
  Water + ice
  All water
  Water + steam
  All steam
Started with the middle condition – all water
If T>100°C, must have some (or all) steam
If T<0°C, must have some (or all) ice
We started here

## Slide 13
equivalent mixer
warmer
1
2
3
Water at 16°C
10. kg/min
Ice at -12°C
4.0 kg/min
Steam at 215°C
6.0 kg/min
cooler
warmer + melter
cooler +
condenser + cooler
2a
3a
3b
Water at 0°C
qcooler
qwarmer+melter
qcondendser+cooler
4
2b
1a
boiler
3c
3d
3e
Water
100°C
qtotal
We predicted water + steam for final product

## Slide 14: Energy Balances
Around the Splitter:
qboiler = qtotal – qwarmer
qboiler = +8423 kJ/min
qboiler
qwarmer
qtotal
warmer
3b
3c
qwarmer
Water
100°C
Around the Warmer:
q3b + qwarmer = q3c
qwarmer = q3c – q3b
= FT,3bCP,water(T3c-T3b)
qwarmer = +8333 kJ/min
Energy goes into heating the water to 100C and then vaporizing the water

## Slide 15: How much water converted to steam?
Balance around Boiler
q3d + qboiler = q3e
qboiler = q3e – q3d = FT,3dΔHvap
FT,3d = qboiler/ΔHvap = 3.7 kg/min
FT,3d ≤ FT,4 so T4 = 100°C
Xsteam = FT,3d/FT,4 = 19 wt% steam
Xwater = 81 wt% water
boiler
3d
3e
qboiler

## Slide 16: Takeaways
Break down complicated processes into simple units.
Check your signs/directionality!
  Is heat entering or leaving the stream?
    Coolers/Condensers → Heat is leaving
    Warmers/Melters/Vaporizers → Heat is entering
Units!
  kJ vs. J
  kg vs. moles (heat capacities)
Questions?