## Slide 1: EngrD 2190 – Lecture 30
Concept: Dimensional Analysis and Dynamic Scaling
Context: Universal Scaling of the Terminal Velocity of a Sphere
Defining Question: What is the most famous dimensionless Group?
Read Chapter 5 pp. 447-454
Dynamic Similarity – How to Design a Model

## Slide 2
Homework
 Homework 9 (the last homework) due Friday 11/21.
5.12 deriving Pi groups
5.26 & 5.31 analysis with dimensionless correlations.
Homework is your chief means of assessing your command of the material.
 Homework 8 due today at noon.
Write team code and names of all contributing team members on all solutions.
Indicate this week’s Team Coordinator.
Submit after lecture or deliver to the EngrD 2190 mailbox in a cabinet in the
hallway outside 116 Olin Hall (ChemE Business Office). Not to my mailbox.

## Slide 3
Homework 7 Excellence – Exercise 4.34 – Team 18
Honorable
Mention to Teams
3, 4, 6, 10, 19, and 23

## Slide 4
Homework 7 Excellence – Exercise 4.46 – Team 19
Honorable
Mention to 18(!) Teams
with perfect scores!

## Slide 5
Homework 7 Excellence – Exercise 4.101 – Team 25
Honorable
Mention to Teams
11, 15, 16, 18, 19, 23, and 26.

## Slide 6
Homework 7 Excellence – Exercise 4.104 – Team 19
Honorable
Mention to Teams
8, 10, 11, 13, 15, 16, 23, 24, and 25.

## Slide 7: Recap
Motivation: to predict the behavior/performance of an inconvenient system.
Inconvenient system is too large or too small.
Inconvenient system is too fast or too slow.
Inconvenient system is too hot or too cold.
Plan: study a convenient model of the inconvenient system.
How to design a dynamically similar convenient model?
Dimensional Analysis and Dynamic Scaling!

## Slide 8: Recap of Dimensional Analysis of Pendulums and Walking
One dimensionless group (of parameters):
The dimensionless group reveals how parameters scale:
If  is increased 100, tperiod increases by 100½ = 10.
Must conduct experiments to obtain universal relation:

## Slide 9: Recap of Dimensional Analysis of Pendulums and Walking, cont’d
Two dimensionless groups:
is called a Dimensionless Group (of Parameters)
aka a Dimensionless Number (The Froude Number)
‘Number’ is a misnomer
aka a P Group
upper case
The magnitude of a dimensionless group describes the phenomenon.
Froude Number < 2.5  bipeds walking or quadrupeds trotting
Froude Number > 2.5  bipeds running or quadrupeds galloping

## Slide 10: Dimensional Analysis and Dynamic Scaling
A Universal Correlation
for the Terminal Velocity of a Sphere

## Slide 11: The Terminal Velocity of a Sphere - Applications
Solid-liquid separations
Muddy water - why does sand settle quickly but silt settles slowly? How slowly?
Solid-vapor separations
Dust settling in air - how long does volcanic ash remain in the atmosphere?
Vapor-liquid systems
How fast do air bubbles rise in a fermenter?
How fast do vapor bubbles rise through the liquid on an equilibrium stage
in a distillation column?
Liquid droplets in air: mist and fog? Spray painting? Virus spreading?
Liquid-liquid systems
Oil-water absorbers and strippers - bouyancy effects?

## Slide 12: The Method of Dimensional Analysis
recap from previous lecture:
1. List parameters
will always be given in this course.
2. Find dimensions of each parameter
3. Write equation for generic P group
4. Choose core variables
5. Derive P groups
6. Measure Data
7. Plot universal correlation

## Slide 13: Dimensional Analysis of a Falling Sphere
will be given
will usually
be given
must derive
dynamics
the sphere
the fluid
physical constant
1. List parameters
2. Find dimensions of each parameter

## Slide 14: Why the density of the fluid is relevant
Consider running
in a straight line
through a crowded room
you
people
‘density’ = people/area
you
people
balloons

## Slide 15: Dimensional Analysis of a Falling Sphere
3. Write an equation
for generic P group
For P to be dimensionless, each dimension’s exponent must be zero.
(6 parameters) - (3 dimensions) = 3 core variables

## Slide 16: Dimensional Analysis of a Falling Sphere
4. Choose core variables
Two Rules for Core Variables
1. The set of core variables must represent all dimensions.
Not velocity, sphere diameter, and gravity (dimension M is omitted).
2. The core variables must not form a dimensionless group.
Not fluid density and buoyancy.
Not velocity, sphere diameter, and gravity:
v2/(dg) is a Froude Number; [v2/(dg)] = (none)
Easy to check.
Not easy to check.
It is often easier
to derive the P groups.
If a problem arises,
this rule was likely
violated.

## Slide 17: Dimensional Analysis of a Falling Sphere
4. Choose core variables, cont’d
Logical choices for the core variables:
What do we want to predict?
velocity
What do we want to vary in our experiments?
sphere diameter and fluid viscosity
But we are not the first to study spheres falling through fluids.
Use traditional core variables to relate our results to previous results.
Traditional core variables: buoyancy, gravity, and fluid viscosity.

## Slide 18: Dimensional Analysis of a Falling Sphere
5. Derive P groups
P = vadb(rsphere - rfluid)cmd(rfluid)egf
Use the core variables - buoyancy, gravity, and fluid viscosity - to set the exponents.
P1
buoyancy
c = 1
gravity
f = 0
fluid viscosity
d = 0
P2
c = 0
f = 1
d = 0
-1
P3
c = 0
f = 0
d = 1
-1
Core variables buoyancy, gravity, and fluid viscosity yield key dimensionless groups!

## Slide 19: Core variables buoyancy, gravity, and fluid viscosity yield key dimensionless groups!

## Slide 20: The Reynolds Number
density  volume = mass
 surface area of sphere
 Shear stress (Newton’s Law of Viscosity)
Re < 1
1 < Re < 1000
Re > 1000
Osborne Reynolds 1883

## Slide 21: The Reynolds Number

## Slide 22: Dimensional Analysis of a Falling Sphere
6. Measure Data
Measure v, d, rsphere, m, and rfluid.

## Slide 23: Dimensional Analysis of a Falling Sphere
7. Plot universal correlation
How to plot? A 3-D plot of a level surface?
Difficult to read
quantitative values.
Better to plot as a
family of curves
for values of Fr.

## Slide 24: Dimensional Analysis of a Falling Sphere
Divide reduced buoyancy
by Froude number
7. Plot universal correlation, cont’d

## Slide 25: Fluid Flow around a Sphere
Re < 1
Laminar Flow
Stokes’s Law
slope = -1
Re > 100
Turbulent Flow

## Slide 26: Dynamically Similar Spheres Falling at their Terminal Velocity
inconvenient
Use convenient models to predict results for inconvenient systems.
Extrapolation?
No! All systems are dynamically similar.

## Slide 27: Flow Around a Cylinder
Re « 1
Re = 100
Re = 1000
Re = 10,000

## Slide 28: Flow Past a Plate
Re = 0.1
Re = 10,000

## Slide 29: Flow Past an Airfoil
Re = 100
Re = 1000

## Slide 30: Flow Past a Block
Re = 0.01
Re = 10
Re = 10,000

## Slide 31: Flow Past a House
Re = 0.1
Re = 10
Re = 100
Re = 10,000